## Slide 1
Edge-AI Line Crossing Detector on NXP i.MX8
Porting, Hardware Offloading, and Optimization of Real-Time Vision Systems
• Presenter: [Your Name]
• Target Hardware: NXP i.MX8M Plus SoC (VIP8000 NPU)
• Focus: Edge ML Inference, GStreamer Hardware Pipelines, Self-Healing Resilience
Notes: Welcome everyone. Today I'll walk through the porting, hardware offloading, and performance optimization of our live line-crossing vision system on the NXP i.MX8 edge platform.

## Slide 2
Initial Prototype & Performance Bottlenecks
Transitioning from Laptop Prototyping to Resource-Constrained Edge Chips
• Initial Prototype: OpenCV Python capture (cv2.VideoCapture) running on a laptop.
• Edge Constraints: Porting to i.MX8 caused CPU usage to hit 85%+ with infinite video lag.
• Initial Attempt (Manual Frame Skipping): Skips every 3rd/5th frame in Python.
• Limitations: Rigid skipping failed when camera framerates or NPU timing fluctuated.
Notes: When I first ported our laptop computer vision prototype to the i.MX8 edge board, CPU usage reached 85%, and the video stream accumulated lag. My first step was writing a manual frame-skipper in Python. However, fixed frame-skipping proved too rigid to handle dynamic camera framerates and inference timing variations.

## Slide 3
Model Quantization & NPU Hardware Delegation
Offloading Neural Network Matrix Operations from CPU to VIP8000 NPU
• Float32 CPU Bottleneck: Standard float32 YOLOv8n execution on CPU took > 400 ms per frame.
• Full-Integer Quantization: Converted model to 8-bit full-integer TFLite (uint8/int8).
• NPU Driver Delegate: Configured TFLite runtime to load NXP libvx_delegate.so driver.
• Performance Impact: Latency dropped to 78.2 ms, holding average NPU load at 21.5%.
Notes: To reduce inference latency, I quantized YOLOv8n to 8-bit full-integer TFLite format. I then configured the TFLite runtime to load NXP's libvx_delegate.so driver, offloading tensor calculations directly to the onboard VIP8000 NPU. This reduced inference latency to 78 milliseconds while using 21.5% of the NPU capacity.

## Slide 4
Pipeline Refinement & Dynamic Frame Dropping
Offloading Colorspace Conversion to GPU & Replacing Manual Frame Skipping
• GPU Colorspace Scaling: Used imxvideoconvert_g2d to offload YUV-to-BGRx scaling to 2D GPU.
• Replaced Manual Skipping: Configured GStreamer appsink with drop=true and max-buffers=1.
• Decoupled Architecture: AppSink dynamically drops stale intermediate frames while NPU is busy.
• Result: Visual streaming rate (11.2 FPS) decoupled from NPU inference rate (6.0 FPS).
Notes: After offloading model execution, I turned to pipeline optimization. First, I offloaded colorspace conversion and scaling to the i.MX8 GPU using GStreamer's imxvideoconvert_g2d element. Next, I replaced the manual frame-skipping logic with GStreamer's appsink element configured with drop=true and max-buffers=1. This dynamically drops stale frames at the buffer boundary, guaranteeing zero video lag while keeping video streaming smooth at 11.2 FPS.

## Slide 5
Boundary Math & False-Positive Elimination
Foot-Point Vectors, EMA Centroid Smoothing, Spatial Padding, and Debouncing
• Foot-Point Tracking: Tracked bottom-center point (x + w/2, y2) to stabilize floor contact.
• EMA Centroid Smoothing: Applied smoothing (alpha=0.75) to eliminate bounding box jitter.
• Vector Cross-Product: Computed 2D signed cross product d(P) = (x - x1)(y2 - y1) - (y - y1)(x2 - x1).
• Spatial & Temporal Filters: 30px spatial buffer padding + 2-frame debouncing state machine.
Notes: To ensure count accuracy, I addressed bounding box jitter near the line. I updated the math to track foot points instead of box centers, applied Exponential Moving Average smoothing to centroids, and added a 30-pixel spatial padding zone with a 2-frame debouncing state machine. This eliminated false counts caused by loitering individuals.

## Slide 6
Industrial Resilience & Fault Tolerance
Handling Hardware Disconnects and Process Recovery Gracefully
• Hardware Disconnect Recovery: Catches Gst.MessageType.ERROR when camera is unplugged.
• Hardware Lock Cleanup: Transitions GStreamer to Gst.State.NULL to release /dev/video3 locks.
• Stepped Backoff: Retries every 3s for 2 minutes (40 retries), then backs off to 3m intervals.
• OS Service Integration: Registered GLib.unix_signal_add(SIGTERM) for 3s systemd auto-recovery.
Notes: For field deployments, I implemented a self-healing layer. If a camera cable is unplugged, our GStreamer bus callback catches the error, releases hardware device locks, and enters a stepped-backoff reconnect loop. If the process is terminated, systemd automatically restarts the service within 3 seconds.

## Slide 7
Benchmarking & System Verification (30.7-Minute Run)
Continuous Stress Testing on Live Camera Streams
• Test Duration: Processed 26,911 frames continuously over 30.7 minutes.
• Visual & Inference Rates: RTSP Output at 11.2 FPS | NPU Inference at 6.0 FPS.
• Hardware Loads: NPU Avg 21.5% (Max 42%) | CPU Avg 47.3% (Max 84%).
• Memory & Thermal Stability: RAM flat at 18.9% (zero leaks) | Temperature stable at 80.6°C.
Notes: I verified system performance with a 30-minute stress test on live camera feeds. The benchmark results confirmed stability: RAM usage remained flat at 18.9% with zero memory leaks, NPU load averaged 21.5%, and CPU temperature stabilized safely at 80.6°C.

## Slide 8
Key Takeaways & Systems Engineering Learnings
Reflections on Hardware-Software Co-Design
• Hardware Profiling First: Measured sysfs and debugfs (/sys/kernel/debug/gc/load) drivers.
• Iterative Architecture: Replaced naive frame-skipping with dynamic appsink ring buffers.
• Production Readiness: Designed self-healing code for OS signals, hardware unplugs, and locks.
• Engineering Growth: Transitioned from writing scripts to building edge ML vision systems.
Notes: Reflecting on this project, my biggest learning was approaching software from a systems perspective—profiling low-level hardware registers, iterating on pipeline architecture, and building resilient code designed for real-world hardware.